## Slide 1: Von Neumann Model
Chapter 4

## Slide 2: Outline
Basic Components
  Memory, Processing Unit, Input & Output, Control Unit
LC-3: An Example von Neumann Machine
Instruction Processing
  The Instruction, The Instruction Cycle
    Fetch, Decode, Evaluate Address, Fetch Operands, Execute, Store Result
Changing the Sequence of Execution
Stopping the Computer

## Slide 3
Harvard Mark I

## Slide 4: Harvard Model

## Slide 5
John von Neumann & EDVAC
Electronic Discrete Variable Automatic Computer

## Slide 6: First Draft of a Report on the EDVAC by John von Neumann, Contract No. W-670-ORD-4926, Between the United States Army Ordnance Department and the University of Pennsylvania Moore School of Electrical Engineering University of Pennsylvania June 30, 1945

## Slide 7: von Neumann Model
INPUT
OUTPUT
CONTROL
PROCESSOR
MEMORY

## Slide 8: The Idea
The central idea in the von Neumann model of computer processing is that the program and data are both stored as sequences of bits in the computer's memory, and the program is executed, one instruction at a time, under the direction of the control unit.

## Slide 9: Splitting Hairs...
There is also a class of architectures called “Modified Harvard Architecture”
These are systems that may treat memory as a single address space, but provide different paths to the CPU for instructions and data, typically to improve performance
That tells us that, just like much of the rest of computer architecture, there is a spectrum of possible architectures between Harvard and von Neumann
Don’t let that worry you

## Slide 10: Some Stats
Harvard Mark I
  Switches, relays, rotating shafts, clutches
  60 sets of 24 decimal switches
  72 adding machines with 23 decimal digits
  Instructions stored on paper tape loop
  3.7 kW electric motor(!)
  3 additions/sec, 6 sec/multiplication
EDVAC
  6,000 vacuum tubes, 12,000 diodes
  Magnetic tape input/output
  1000 44-bit words in 128 acoustic delay lines
  56 kW power
  1160 additions/second, 340 multiplications/sec

## Slide 11: Machine Instructions as Data?
The von Neumann model leads us to treat machine instructions as just another data representation!
Think unsigned integer, twos-complement integer, ASCII, IEEE-754 floating point, ..., and machine instructions

## Slide 12: Memory
What is stored in memory?
How many memories do we need?

## Slide 13: Memory
MAR
MDR
ADDR
DATA IN
DATA OUT
OUT
IN
OUT
IN
WE
MUX
16

## Slide 14: von Neumann Model
INPUT
OUTPUT
MDR
MAR
CONTROL
PROCESSOR
MEMORY

## Slide 15
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor

## Slide 16: Situational Awareness
Knowing Where Things Are

## Slide 18: Issues
Memory
  MAR, MDR
Processing Unit
  Register File, ALU (size)
Input and Output
  KBDR, KBSR, DDR, DSR
Control
  FSM, PC (Next Instruction Pointer), IR

## Slide 19: What is a Machine Instruction?

## Slide 20: Test Yourself
The Program Counter (PC) holds
  The count of instructions executed
  The address of the next instruction to be executed
  The instruction currently being executed
  Number of programs completed since the last boot

## Slide 21: Test Yourself
The Instruction Register (IR) holds
  All legal op codes
  The address of the next instruction to be executed
  The instruction currently being executed
  All data needed to execute the current instruction

## Slide 22: LC-3 CPU
Address space
  216 = 65536
Addressability
  16 bits
Architecture type
  Von Neumann
General purpose registers
  8
Instruction size
  16 bits

## Slide 23: LC-3 Instructions
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
ADD
1

## Slide 24
0001
DR
SR1
0
00
SR2
ADD+
0101
DR
SR1
0
00
SR2
AND+
0001
DR
SR1
1
imm5
ADD+
0101
DR
SR1
1
imm5
AND+
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
LD+
0010
PCoffset9
DR
LDI+
1010
PCoffset9
DR
+ Indicates instructions that modify condition codes

## Slide 25: Instruction Example
0
0
0
0
1
0
0
0
1
0
0
0
0
1
1
ADD
1
ADD R2,R1,R3
R2
R1
R3
0x1443
012103

## Slide 26: Instruction Cycle
Fetch
Decode
Evaluate Address [optional]
Fetch Operands [optional]
Execute [optional]
Store Result [optional]
EA
OP
EX
S
F
D

## Slide 27: Before We Look at the Data Path During the Instruction Cycle...
There are 39 control signals orchestrated by the FSM
The wires don’t fully show up in the datapath diagram, but the signals have names
Multiplexor selectors
  PCMUX, MARMUX, ADDR2MUX, …
Tri-state buffer enables
  gatePC, gateMARMUX, gateALU,…
Register write enables
  LD.PC, LD.REG, LD.MAR, LD.CC, …
Others
  ALUK, MEM.EN, R.W, …

## Slide 28: Register File Circuit
“Memory” with 8 16-bit locations
Two output controllers
  SR1 (3 bits)
  SR2 (3 bits)
One input controller
  DR (3 bits)
  LD.REG
Cycles with the CPU clock

## Slide 29: Program Counter Circuit
PCMUX
  Adder to increment PC
  Data from bus to PC
  Data from effective address calculator to PC

## Slide 30: Instruction Processing: FETCH
Load next instruction (at address stored in PC) from memory into Instruction Register (IR).
  Copy contents of PC into MAR.
  Send “read” signal to memory.
  Copy contents of MDR into IR.
Increment PC, so that it points to the next instruction in sequence.
  PC becomes PC+1.
EA
OP
EX
S
F
D

## Slide 31
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
FETCH
2

## Slide 32: Instruction Processing: DECODE
First identify the opcode.
  In LC-3, this is always the first four bits of instruction.
  The FSM chooses a next state corresponding to the desired opcode.
Depending on opcode, identify other operands from the remaining bits.
  Example:
    for LDR, last six bits is offset
    for ADD, last three bits is source operand #2
EA
OP
EX
S
F
D

## Slide 33
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
DECODE

## Slide 34: Instruction Processing: EVALUATE ADDRESS
For instructions that require memory access, compute address used for access.
Examples:
  add offset to base register (as in LDR)
  add offset to PC
  add offset to zero
EA
OP
EX
S
F
D

## Slide 35
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
EVALUATE ADDRESS
(Addresses are registers; nothing to calculate)

## Slide 36: Instruction Processing: FETCH OPERANDS
Obtain source operands from memory needed to execute the operation.
Examples:
  load data from memory (LDR)
  bring data from a register (unless the CPU can do that during EXECUTE like the LC-3)
EA
OP
EX
S
F
D

## Slide 37
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
FETCH OPERANDS
(Operands in registers; nothing to fetch)

## Slide 38: Instruction Processing: EXECUTE
Perform the operation, using the source operands.
Examples:
  send operands to ALU and assert ADD control signal
  do nothing (e.g., for loads and stores)
EA
OP
EX
S
F
D

## Slide 39
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
EXECUTE
3
2
1
1
0
+

## Slide 40: Instruction Processing: STORE RESULT
Write results to memory (or a register if the CPU doesn’t do that as part of EXECUTE)
Examples:
  for store instruction, data is stored to memory
    write address to MAR, data to MDR
    assert WRITE signal to memory
  for ADD instruction, store the result in the destination register if not done in EXECUTE
EA
OP
EX
S
F
D

## Slide 41
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
STORE RESULT

## Slide 42: Instruction Processing Summary
Instructions look just like data – it’s all interpretation.
Three basic kinds of instructions:
  computational instructions (ADD, AND, …)
  data movement instructions (LD, ST, …)
  control instructions (JMP, BRnz, …)
Six basic phases of instruction processing: F  D  EA  OP  EX  S
  not all phases are needed by every instruction
  phases may take variable number of machine cycles

## Slide 43: Control Unit State Diagram
The control unit is a state machine. Here is part of a simplified state diagram for the LC-3:
A more complete state diagram is in Appendix C.
It will be more understandable after Chapter 5.
18
33
35
1
6
12
32

## Slide 44: LC-3 Finite State Machine p. 568, Fig C.3

## Slide 45: Changing the Sequence of Instructions
In the FETCH phase, we increment the Program Counter by 1.
What if we don’t want to execute the instruction that follows this one?
  examples: loop, if-then, function call
We need special instructions that change the contents of the PC.
These are called control instructions.
  jumps are unconditional -- they always change the PC
  branches are conditional -- they change the PC only if some condition is true (e.g., the result of an ADD is zero)

## Slide 46: Example: LC-3 JMP Instruction
Set the PC to the value contained in a register. This becomes the address of the next instruction to fetch.
“Move the contents of R3 into the PC.”

## Slide 47
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
EXECUTE
3
1

## Slide 48: Stopping the Clock
Control unit will repeat instruction processing sequence as long as clock is running.
  If not processing instructions from your application, then it is processing instructions from the Operating System (OS).
  The OS is a special program that manages processor and other resources.
To stop the computer:
  AND the clock generator signal with ZERO
  When control unit stops seeing the CLOCK signal, it stops processing.

## Slide 49: Instructions
0
0
0
0
0
0
0
0
0
0
0
0
0
0
LDR
1
1

## Slide 50: Which is better?

## Slide 52: Treasure Map

## Slide 53
+1
PC
FINITE
STATE
MACHINE
SEXT
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
INPUT
OUTPUT
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
MARMUX
ADDR2MUX
ADDR1MUX
PCMUX
+
SEXT
SEXT
ZEXT
N
Z
P
LOGIC
SEXT
16
gateMARMUX
IR
16
LD.MAR
16
gateALU
R
[10:0]
[8:0]
[5:0]
[4:0]
0
16
16
16
16
LD.CC
16
16
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
16
LD.IR
[7:0]
2
2
LD.PC
ADDR2MUX
ADDR1MUX
16
16
16
2
16
A
B
MARMUX
PCMUX

## Slide 54: Flow Control
Normally we execute instructions one after another
Test Yourself
When might we not want to do this?
  Tuesdays
  During compilation
  When branching, jumping or looping
  When playing pirated games

## Slide 55: Instructions
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
JMP

## Slide 56
+1
PC
FINITE
STATE
MACHINE
SEXT
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
INPUT
OUTPUT
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
MARMUX
ADDR2MUX
ADDR1MUX
PCMUX
+
SEXT
SEXT
ZEXT
N
Z
P
LOGIC
SEXT
16
gateMARMUX
IR
16
LD.MAR
16
gateALU
R
[10:0]
[8:0]
[5:0]
[4:0]
0
16
16
16
16
LD.CC
16
16
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
16
LD.IR
[7:0]
2
2
LD.PC
ADDR2MUX
ADDR1MUX
16
16
16
2
16
A
B
MARMUX
PCMUX

## Slide 57: Stopping
Clock
S
R

## Slide 58
+1
PC
FINITE
STATE
MACHINE
SEXT
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
INPUT
OUTPUT
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
MARMUX
ADDR2MUX
ADDR1MUX
PCMUX
+
SEXT
SEXT
ZEXT
N
Z
P
LOGIC
SEXT
16
gateMARMUX
IR
16
LD.MAR
16
gateALU
R
[10:0]
[8:0]
[5:0]
[4:0]
0
16
16
16
16
LD.CC
16
16
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
16
LD.IR
[7:0]
2
2
LD.PC
ADDR2MUX
ADDR1MUX
16
16
16
2
16
A
B
MARMUX
PCMUX

## Slide 59: Questions